## Flat-frame Construction materials worksheet

Listed below are some hardwoods and softwoods commonly used in flat-frame construction. Complete the table by:

1	Identifying and correctly naming the listed woods in the workshop

2	Describing the appearance and type of wood (hardwood or softwood)

2	Describing the properties of each type of hardwood/softwood in terms of: strength; cost; water resistance, ease of working/cutting/shaping

| Wood | ID ( | Hardwood or softwood and appearance | Properties |
| --- | --- | --- | --- |
| White Pine |  |  |  |
| Red Pine |  |  |  |
| Cedar |  |  |  |
| Larch |  |  |  |
| Ash |  |  |  |
| Oak |  |  |  |
| Beech |  |  |  |
| Mahogany/ Meranti |  |  |  |

Candidate signature: ___________________________________________

Completion date: ______________________________________________

Assessor signature: ______________________________________________

Date: ________________________________________________________

| Flat-frame practice joint (template) Name of joint:__________________________________________ |
| --- |
| Picture/ image/tracing/ sketch: |
| What tools did you use in the preparation and construction of this joint? |  |
| What (if any) mechanical fixings or adhesives did you use in the construction of this joint? |  |
| What safe working practices did you employ in the construction of this joint? |  |

Candidate signature: ___________________________________________

Completion date: _______________________________________________

## Example of a flat-frame assembly model

Shoe Stand

The shoe stand is manufactured in two parts. Frame A (top section) and Frame B (base section). The frames are joined together using an appropriate mechanical fixing. A small bracket or hinge would best serve this purpose.

|  |  | Part | Quantity | Material | Length | Breadth | Width |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | A | 1 | Any appropriate softwood, hardwood or manufactured board | 400 | 50 | 18 |
|  |  | B | 2 |  | 182 | 30 | 18 |
|  |  | C | 1 |  | 400 | 30 | 18 |
|  |  | D | 1 |  | 400 | 30 | 18 |
|  |  | Part A to B — Dowel joint Part D to B — A selection of joints are available for use National 5 — T-Halving, bridle, mortise and tenon (stub or through) Part C to B — National 5 — mitre |
| Frame A — National 5 |  | © SQA |  |  |

Shoe Stand - Frame B

| © SQA |  | Part | Quantity | Material | Length | Breadth | Width |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | E | 2 | Any appropriate softwood or hardwood | 100 | 30 | 18 |
|  |  | F | 2 |  | 202 | 30 | 18 |
|  |  | G | 2 |  | 50 | 30 | 18 |
|  |  | H | 1 |  | 400 | 30 | 18 |
|  |  | Parts E to F — cross halving or an appropriate mechanical fixing method Parts G to F — cross halving Part H to F — a selection of joints are available for use. National 5 — T-Halving, bridle, mortise and tenon (stub or through) |
| © SQA |  |  |

| Assembled flat-frame model |
| --- |
| Name of model: |
| Were all components of the model included in accordance with the cutting list? |  |
| What tools did you use in the preparation and construction of this model? |  |
| Were any adjustments to tools required before, during or after use? |  |
| What (if any) mechanical fixings or adhesives did you use in the construction of this model? |  |
| What safe working practices did you employ in the construction of this model? |  |

Candidate signature: ____________________________________

Completion date: _______________________________________